Unfiltered data

---
Processing steps:
Find intervals with stable magnetic field at maximum value (around 3.8 T)
Find the mode in voltage value for each luminosity value.
Smooth the data
Find deviation from each averaged data point
Calculate flux/dose from voltage

---
Smoothing algorithm
- Walk through data points, keeping track of “current” stable voltage value and assign points to it until a new stable value is found.
- Value will be considered stable if it occurs more than w amount of times consecutively.

---
Filtered magnetic field

---
Filtered voltage

---
Voltage to flux/dose
dose=(%DELTA U/0.01854)^{ 1 over 0.91072 }
flux=2.105 times 10^11 %DELTA U

---
Voltage to flux

---
Flux comparison

---
Flux comparison

---
Dose comparison

---
Dose comparison